Complexity
# Introduction
In this practical we will be looking at how the performance of a vanilla quicksort implementation varies according to the ‘sortedness’ of a list. This report should lay out how I implemented quicksort, a brief discussion of measures of sortedness and the input lists I will be testing, an examination of how quicksort speeds up (or slows down) depending on the sortedness of the list and the choice of pivot, and different measures for its efficiency.
# Design
## Quicksort
The implementation of quicksort we’ll be examining here is the not-in-place version that makes use of new, smaller and smaller lists before recombining rather than the in-place version that makes of use of pointers to the larger list. The main factor that will influence the speed of quicksort is its choice of pivot at each splitting of the list as every element will be compared to that pivot. There are 3 common choices here, the first element of the list, the median element, or the last element. As making the pivot first or last would be functionally identical or close to it for a random list, I will only examine a median pivot or first element pivot.
## Sortedness of a List
There are a number of methods to define how ‘sorted’ a list is:
Example List: W1 ={ 5, 8, 10, 9, 11, 6, 7,4}
1. Distance. The distance of an swap of two elements of a list. A larger swap is more disordered than a shorter one (Estivill-Castro, Wood 1992). e.g when looking at (5, 6) it would have a Dis(W1) of 5.
2. Max. The maximum distance an element has to travel to reach its sorted position (Estivill-Castro, Wood 1992). e.g 4 has to travel seven positions to reach its sorted position.
3. Exchange. The minimum number of exchanges required to sort a sequence (Estivill-Castro, Wood 1992).
4. Rem. The the minimum number of elements that must be re-moved to obtain a sorted subsequence (Estivill-Castro, Wood 1992).
5. Runs. The number of boundaries between ascendings runs of numbers within the list (Estivill-Castro, Wood 1992). e.g. W1 ={ 5, 8, 10 || 9, 11|| 6, 7|| 4} therefore it has 3 runs.
This is important when considering test cases for the quicksort algorithm in order to acquire a more precise scientific definition of ‘sorted’ for testing purposes. For the purposes of this report I decided to use the method described by Curtis & Kim in ‘Best Sorting Algorithm for nearly sorted lists’ and define a ‘sortedness ratio’ of a list as the Rem. Value over the total length of a list (Curtis & Kim 1980). This produces a value between 0 and 1, with 0 being a totally sorted list and values approaching 1 representing a randomly ordered list.
I chose this measure for its simplicity and because there is readily available algorithm that can calculate the longest ascending sequence in a list thereby making calculating the sortedness ratio, and producing lists of a specific sortedness ratio trivial.
# Implementation
## Input Lists

Bibliography
https://cs.stackexchange.com/questions/22516/why-is-quicksort-described-as-in-place-if-the-sublists-take-up-quite-a-bit-of

Curtis, CR and Kim, DJ. (1980). Best Sorting Algorithm for Nearly Sorted Lists. Communications of the ACM. 23 (Issue 11), 620-621.
Estivill-Castro, V & Wood, D. (1992). A Survey of Adaptive Sorting Algorithms. ACM Computing Surveys (CSUR). 24 (Issue 4), p. 447.